## Slide 1: Mathematical Model Details

## Slide 2: Overview
PID
Appropriate Summations
PID
PID
PID
PID
PID
Duty Cycle to PWM
Duty Cycle to PWM
Duty Cycle to PWM
Duty Cycle to PWM
Drone
+
-
+
-
+
-
+
-
Desired Yaw
Desired Elevation
Desired XY Position
Conversions (If Necessary)
+
-
+
-
Motor PWM Values
Sensor Feedback (May need to operations with these when feeding back)
Desired Pitch
Desired Roll

## Slide 3: PID Variables
e[]
  Array of size ??? holding error values from sampled sensor values.
  Most recent value is held at the end(?)
P, I, and D
  Gain values for each part of the PID controller.
sum
  “Integration” of e[] (see “Integral Details” slide)
slope
  “Derivative” of e[] (see “Derivative Details” slide)
dutyCycle
  Final output: gives the Duty Cycle of the PWM signal that needs to be generated (valued from 0 to 255, NOT 100. Because that’s the way the 8-bit-resolution-pwm-cookie crème brûlées)
PID

## Slide 4: Duty Cycle Calculation
dutyCycle = P*e[last] + I*sum – D*slope
if(dutyCycle > 255) {
dutyCycle = 255;
}
PID

## Slide 5: Integral Details
sum will keep track of the integration so far.
for each new sample:
  sum += e[last] //assuming the most recent element is in the last position
Additional operations needed to correct overshoot (see “Overshoot Correction”)
PID

## Slide 6: Derivative Details
2 Options to solve for slope (2 is probably best)
ACTUALLY, 1 might be best if we downsample before getting error values.
(most recent e) – (2nd most recent e)
  Pros:
    More responsive
  Cons:
    Noise can really mess stuff up, and can also be twitchy
(average of N most recent or e[]) – (average of the next N of e[])
  Pros:
    Resists noise effects
  Cons:
    Slower response
PID

## Slide 7: MORE Derivative Details
Suppose we do option 2 with N = 2:
Old :
Now, we shift in the new error, n:
NOTE: I didn’t simplify the 2b, because the 2 coefficient will not change with the 2 in the denominator.
Other note: forget this stuff, we’ll just average and filter before sending the error to the function.
PID

## Slide 8: Overshoot Correction
Need to cap sum to some value.
255 would work but we could probably cap it at a smaller value.
PID

## Slide 9: Appropriate Summations
Mfr = a*Thrust + b*Yaw + b*Pitch + b*Roll
Mfl = a*Thrust - b*Yaw + b*Pitch - b*Roll
Mbr = a*Thrust - b*Yaw - b*Pitch + b*Roll
Mbl = a*Thrust + b*Yaw - b*Pitch - b*Roll
Note: a+3b = 1
This should keep the final values between 0 and 255 (crème brûlée)
Appropriate Summations

## Slide 10: Duty Cycle to PWM Block
Duty Cycle to PWM
Things to keep in mind:
  TDutyCycle <= Tsample
  TDutyCycle should be some multiple of Tsample